## Slide 1: D-STAR Operations 101
Ed Woodrick WA4YIH

## Slide 2: D-STAR Functions
What Can I Do?

## Slide 3: Local
This is WA4YIH, anyone around?
WA4YIH this is WB4QDX
How are you doing?

## Slide 4: Local – with Gateway
This is WA4YIH, anyone around?
WA4YIH this is WB4QDX
How are you doing?
WA4YIH this is KJ4G
Also listening

## Slide 5: Linked Repeaters
This is WA4YIH
Anyone around?
This is WA4YIH
Anyone around?
This is WA4YIH
Anyone around?
This is WA4YIH
Anyone around?
This is WA4YIH
Anyone around?
I’m here
I’m here
I’m here
I’m just listening

## Slide 6: Talking D-STAR
Overcoming one of the hardest obstacles in Amateur Radio.
Programming your radio!

## Slide 7: Programming Radios
In the Old Days…
  Frequency Setting
    Crystal (had to buy each channel)
    Thumbwheel (single frequency)
    Multiple Memories
  PL Support
    After market board with DIP switches
    Manufacturer supplied boards
    Built-in to radio

## Slide 8: Programming Radios Today
Each Manufacturer uses different methods
Each Radio is different
Lots of channels are tedious to program and hard to edit
Software makes it easier

## Slide 9: FM Repeaters
Name
Frequency
Offset (direction and amount)
Tone (encode and/or decode) (CTCSS or DCS)
Linkable?
  IRLP
  EchoLink

## Slide 10: D-STAR Repeaters
Name
Frequency
Offset (direction and amount)
Mode
Repeater Call Signs

## Slide 11: D-STAR Call Sign Fields
URs is MYne and MYne is URs.

## Slide 12: Basic D-STAR Programming
Set Frequency
Set Offset direction and amount
Set Mode
Set Your call sign in MY field
Place CQCQCQ in UR field
Set repeater call sign in RPT1 and RPT2 fields
  In last character (8th) of the RPT1, place module
  In last character (8th) of the RPT2, place “G”

## Slide 13: Module Lettering Standards
Supported Worldwide, except Japan
  1.2 GHz Voice A
  440 MHz Voice B
  144 MHz Voice C

## Slide 14: Sample – Basic Repeater
Sample for KJ4BDF Repeater 440.725 MHz +5.0 MHz Offset
  MY WA4YIH
  UR CQCQCQ
  RPT1 KJ4BDF▪B
  RPT2 KJ4BDF▪G
"▪" represents a space

## Slide 15: Taking the Next Step
What else can I do?

## Slide 16: DPLUS Functions
G – Gateway
E - Echo Test
I – Identification
L – Link Repeater
U – Unlink Repeater

## Slide 17: Sample – Echo Test
Sample for KJ4BDF Repeater 440.725 MHz +5.0 MHz Offset
  MY WA4YIH
  UR ▪▪▪▪▪▪▪E
  RPT1 KJ4BDF▪B
  RPT2 KJ4BDF▪G
"▪" represents a space

## Slide 18: Sample – Linking
Sample for KJ4BDF Repeater 440.725 MHz +5.0 MHz Offset
  MY WA4YIH
  UR REF002AL
  RPT1 KJ4BDF▪B
  RPT2 KJ4BDF▪G
"▪" represents a space

## Slide 19: Sample – UnLinking
Sample for KJ4BDF Repeater 440.725 MHz +5.0 MHz Offset
  MY WA4YIH
  UR ▪▪▪▪▪▪▪U
  RPT1 KJ4BDF▪B
  RPT2 KJ4BDF▪G
"▪" represents a space

## Slide 20: Call Sign Routing
Sample for KJ4BDF Repeater 440.725 MHz +5.0 MHz Offset
  MY WA4YIH
  UR WB4QDX▪▪
  RPT1 KJ4BDF▪B
  RPT2 KJ4BDF▪G
"▪" represents a space

## Slide 21: Programming Memories
Make it easy on yourself

## Slide 22: Organize Your Memories

## Slide 23: One Touch Repeater Operation

## Slide 24: Programming Your Radio
Set VFO Mode (not memory)
Enter Frequency
Set DUP to + or –
Set Offset if non-standard (0.6 MHz for 2M, 5.0 MHz for 440)
Set Mode to DV (FM, FM-N, AM, DV)
Key Radio

## Slide 25: After Keying Radio
After a second, repeater will respond
Repeater Call Sign Auto Write turned on
  or
Press the One Touch (RX->CS) Key
Repeater Information will be written to temporary Call Signs
“G” may not be written into RPT2, but you will be able to talk to local users

## Slide 26: Resources
www.DSTARInfo.com
  D-STAR Calculator
  D-STAR Listings
  D-STAR Maps
  Closest Repeaters Map
www.DSTARUsers.org
  Last Heard List
  D-STAR Listings