## Slide 1: D-STAR InfoCon 2016 at Dayton Hamvention Part 3 – Doing More With D-STAR
John Davis WB4QDX

## Slide 2: D-STAR’s 1.2 GHz Radio
Icom ID-1
Operates FM Voice or GMSK (D-STAR) modes
D-STAR modes include voice, low speed data (1200 bps) or high speed data (128 kbps)
10W transmit output

## Slide 3: ID-1 High Speed Data Mode
Radio acts as Ethernet wireless bridge
Has RJ-45 Ethernet connector for HS data
Can be used for Internet connectivity through D-STAR repeater with DD module
Can be used to create wireless bridge between two points
When communicating through DD repeater, know assigned IP address (10.x.x.x)

## Slide 4: High Speed Data – DD Mode
Ethernet connection to PC
PC must use assigned IP address assigned at registration (10.x.x.x)
Gateway is 10.0.0.1
Use known DNS addresses
…or the easy way is to insert a router between ID-1 and PC and use DHCP!

## Slide 5: Setup With Router
ID-1
Radio
Router
PC
LAN
DHCP Enabled
192.168.0.x
WAN
IP: 10.x.x.x / 255.0.0.0
Gateway: 10.0.0.1
DNS: Use any DNS
PC
Wired or Wi-Fi
DHCP Enabled
Radio Programming
UR: WD4STR
RPT1: WD4STR A
RPT2: WD4STR G
Mode: RPS

## Slide 6: DV Dongles
Different styles available from Internet Labs (DV Dongle), NW Digital (Thumb DV) and MoenComm (Star*DV)
Attaches to USB port on PC
Accesses D-STAR network using sound card in PC connected to Internet
A new Dongle product to be announced in D-STAR Forum today

## Slide 7: DVAPs
DV Access Point is low power hotspot providing radio access to D-STAR network through PC
Developed by Internet Labs (Robin Cutshaw, AA4RC)
Connects to PC, Raspberry Pi by USB
10mW RF power for 100m range
D-STAR radio uses standard commands for linking
Software on PC, Pi (DVAPtool or DVAPnode)
Internet access on PC, Pi to network

## Slide 8: Using a DVAP
Normal connection to DVAP is a PC, Laptop or Netbook (bulky) with Internet connection

## Slide 9: Add a Raspberry Pi?
Credit card sized Linux computer with SD Card slot, 2 USB, Ethernet and HDMI ports powered by 5VDC micro-USB adapter

## Slide 10: Homebrew DVAP Package
USB CLA (12V to 5V USB)
Micro-USB Cable
USB Adapter (120VAC to 5V USB)
USB Charger/5VDC Supply Anker 10,000 mAH or equivalent
DV Access Point
Raspberry Pi Model B
Pelican 1050 or 1060 Case

## Slide 11: Making It Work
Download image file and instructions
  DVAPtool version: https://www.dropbox.com/sh/mfyw3j6dwkpmriz/V56pE5JqTL
  ircDDB version: http://www.westerndstar.co.uk/Downloads/DVAP+ircDDB+VNC.rar or
  http://maryland-dstar.org/html/raspberry.html
Install OS image to SD card using Win32DiskImager
Power up Pi with SD card installed, HDMI monitor, keyboard, mouse and Internet connection (Ethernet or Wi-Fi)
Configure DVAPtool or DVAPnode and ircDDB per instructions
Configure WiFi sources (Mobile Hotspots, home WiFi, etc)
Can run “headless” after that…just power up, finds defined WiFi sources

## Slide 12: DV Mega
Low power hotspot similar to DVAP (single or dual band versions)
Attaches to Raspberry Pi GPIO connector (Pi Model B, B+, Pi 2) or Arduino
SD card with OS and ircDDBgateway software
Use Wi-Fi dongle or wired Ethernet
Micro USB power to AC or DC source
Use ircDDBgateway SD card images from Maryland D-STAR and Western D-STAR
New DVmega BlueSpot supports multi-mode (D-STAR, DMR)
http://www.dvmega.auria.nl/

## Slide 13: DHAP
Commercially available from Hardened Power Systems http://www.portableuniversalpower.com/DHAP.htm
Includes case, battery, Raspberry Pi
User supplies DVAP (2m or 70cm)

## Slide 14: DHAP Mini Mega
Two versions available for DVAP or DV Mega
Commercially available from Hardened Power Systems http://www.portableuniversalpower.com/DHAP.htm
Includes case, battery, Raspberry Pi
User supplies DVAP or DV Mega

## Slide 15: Multi-mode Devices DV4mini
DVAP type device on USB stick
SMA RF connection to antenna
100 mw transmitter
Compatible with D-STAR, DMR and Fusion
Available from Wireless Holdings http://wirelesshold.com/

## Slide 16: DV4mobile
Software defined mobile radio (2m, 220, 70cm)
Cable of FM plus multiple digital modes including D-STAR, DMR+, P25, NXDN
Manufacturer says available 4Q 2016
To be available through Wireless Holdings http://wirelesshold.com/

## Slide 17: D-STAR on HF
Icom IC-7100 and IC-9100 are both DV capable on HF
Operates at similar bandwidth to AM
D-STAR HF nets now operating several nights a week
Net info at http://www.dstarinfo.com/DSTARHFNet.aspx

## Slide 18: D-STAR Android App
Remote control app for certain Icom radios (ID-5100, ID-31, ID-51, IC-7100)
Connect by OPC-2350LU cable or Bluetooth to Android device
DR function control
Text messaging
Map
Send/receive photos (camera or file)
RX history

## Slide 19: DV Pro
PC application to display radio information
Works with ID-51 AE, ID-51 Plus and ID-5100 radios
Useful for monitoring, D-STAR Net NCS, radio control
Data cable connects PC to radio
Free download at www.dstarinfo.com/dv-pro.aspx

## Slide 20: D-RATS for Data
D-RATS is full featured program for D-STAR data
Features messaging, forms, file transfer and mapping
May be used with D-STAR radio or Internet
Runs on Windows, Mac or Linux
www.d-rats.com

## Slide 21
Anyone ready to take home an
ID-51A Plus handheld?